## Slide 1
DDCA / DIGITAL ELECTRONICS PROJECT
Design and Simulation of a Digital Door Access System
Using Combinational Logic
Team: Arjun, Joshi, Praneeth, Gnanavardhan
Roll No: 2620040117, 2620090010, 2620090012, 2620090133
Section: 5
Faculty: Dr. Venkat Isampalli
Institution: KLH University]
Roll No: 2620040117, 2620090133, 2620090012, 2620090010

## Slide 3
System Overview
Automated access via combinational logic.
Four binary inputs represent distinct security conditions. The system evaluates these inputs simultaneously to output a final access decision.
Security Guard Analogy
If every required condition is satisfied, access is granted. If even one condition fails, access is denied.
Four binary inputs.
Input 2 is inverted.
Evaluated by one AND gate.

## Slide 4
Why Combinational Logic?
Combinational Logic
Output depends only on present inputs.
Sequential Logic
Output depends on present inputs and previous states.
Instant response.
No clock required.
No memory needed.
Direct I/O relationship.

## Slide 5
System Inputs & Conditions
Binary values dictate states: 1 = Condition Satisfied (HIGH), 0 = Condition Not Satisfied (LOW).
Input 1
1
Input 2
0
Requires inversion.
Input 3
1
Input 4
1

## Slide 6
Hardware Components
Four Input Pins
Generate 0 or 1 signals representing real-world sensor states.
One NOT Gate
Performs logical inversion specifically on Input 2.
4-Input AND Gate
Validates all conditions simultaneously. Outputs 1 only if all inputs are 1.
Door Access Indicator
Displays the final logical decision (Access Granted / Denied).

## Slide 7
Input 2 (I₂) | NOT Input 2 (I₂')
0 | 1
1 | 0
The Role of the NOT Gate
The Reverse Condition
The required state for Input 2 is 0.
However, the final AND gate requires a HIGH (1) signal to validate a condition.
I₂ = 0 → NOT Gate → 1 → Condition Satisfied.

## Slide 8
The Decision Maker: AND Gate
The output is 1 only when A=1, B=0, C=1, and D=1.
In our specific system:
The gate evaluates I₁, I₂', I₃, and I₄. All required conditions must be satisfied simultaneously for access.

## Slide 9
Deriving the Boolean Expression
Step 1: Define inputs.
Input 1 → I₁
Input 2 (must be 0) → I₂'
Input 3 → I₃
Input 4 → I₄
FINAL EXPRESSION
D = Door Access, ' = NOT, · = AND
Success Proof: D = 1 · 0 · 1 · 1 = 1

## Slide 10
I₁ | I₂ | I₃ | I₄ | I₂' (Internal) | Door Access (D)
0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0
System Truth Table Verification
*Showing 6 representative rows out of 16 possible combinations.

## Slide 12
Logisim Implementation Steps
Direct Translation Expression → Hardware
1
Place and label four input components.
2
Place a NOT gate directly after Input 2.
3
Connect I₁, I₂', I₃, and I₄ to the AND gate.
4
Connect AND output to the Door Access indicator.

## Slide 13
Actual Logisim Circuit Showcase
CURRENT STATE OBSERVATION
Access Granted
The screenshot currently has: I1 = 1 I2 = 0 I3 = 1 I4 = 1
Door Access = 1

## Slide 14
Circuit Testing Results
Only one specific combination satisfies all four required conditions.
TEST CASE 1
I: 0 0 0 0
TEST CASE 2
I: 1 0 1 1
TEST CASE 3
I: 1 1 1 1
TEST CASE 4
I: 1 0 1 0
D = 0
Access denied.
D = 1
Access granted.
(I₂' becomes 0)
D = 0
Access denied.
D = 0
Access denied.

## Slide 15
System Architecture Flow
The circuit receives four digital inputs. Input 2 is inverted because its required condition is LOW. The four resulting conditions are then evaluated by the AND gate. Only when every required condition is HIGH does the Door Access output become HIGH.
INPUTS I₁, I₂, I₃, I₄
NOT GATE Inverts I₂
AND GATE Evaluates I₁, I₂', I₃, I₄
OUTPUT Decision

## Slide 16
Design Effectiveness
Key Advantages
Simple architecture: Minimal components required.
Fast response: Instantaneous propagation delay.
No clock required: Operates purely on state changes.
Easy troubleshooting: Direct input-to-output relationship.
Educational clarity: Clearly demonstrates Boolean logic.
Proof of Effectiveness
The circuit is highly effective at implementing the exact access rule defined by the Boolean expression. Its reliability is proven by the truth table and validated through Logisim simulation testing.

## Slide 17
Limitations & Future Scope
Current Limitations
Future Enhancements
× Fixed access conditions.
× No user identification/authentication.
× No password storage or database.
× No event logging or invalid-attempt alarms.
× Not suitable as a complete commercial system.
+ Keypad, RFID, or Biometric integration.
+ Microcontroller integration for dynamic rules.
+ LCD/OLED status display interfaces.
+ Sequential logic for temporary access states.
+ IoT monitoring and remote management.

## Slide 18
Project Conclusion
4 Inputs + 1 NOT Gate + 1 AND Gate = Access Decision
This project demonstrates that even a practical security decision can be represented, verified, and simulated using fundamental combinational logic.
Thank You